TENDER SPECIFICATION

| Contents of the CD in English (German version available on request) | Usability of the sub-structure | Page |
| --- | --- | --- |
| Table of contents |  | 1 |
| A) General Preliminary Remarks |  | 4 – 5 |
| B) Description of Works and Services |  | 6 |
| C) Relevant Standards and Directives |  | 6 |
| Sub-structure systems |  | 7 – 91 |
| 1) ATK 100 “Minor“ | Large-format facade panels, visibly riveted (‘face fixed’) or bonded. | 7 – 8 |
| 2) ATK 100 ZeLa | Large-format facade panels, visibly riveted (‘face fixed’) or bonded | 9 – 10 |
| 3) ATK 100 Thermokonsole | Large-format facade panels, visibly riveted (‘face fixed’) or bonded | 11 – 12 |
| 4) ATK 100 KL and KL-L | Ceramic and fine-stoneware panels with visible clamp fixings | 13 – 14 |
| 5) ATK 101 | Large-format facade panels, visibly riveted (‘face fixed’) or bonded | 15 – 16 |
| 6) ATK 102 “Minor“ | Ceramic and fine-stoneware panels with visible clamp fixings | 17 – 18 |
| 7) ATK 102 | Ceramic and fine-stoneware panels with visible clamp fixings | 19 – 20 |
| 8) ATK 102-GH | Toughened safety glass and photovoltaic glass panels with visible clamp fixings | 21 – 22 |
| 9) ATK 106 SZ 20 | Aluminium coffers with concealed fixings | 23 – 25 |
| 10) ATK 107 B | Aluminium coffers with inset bolt fixings | 26 – 27 |

| Contents | Usability of the Sub-Structure | Page |
| --- | --- | --- |
| 11) ATK 601 G | Large-format facade panels, visibly riveted | 28 – 29 |
| 12) Wood holders, type H1 | Large-format facade panels, face fixed with screws | 30 – 31 |
| 14) Wood holders, type T1, T2 | Large-format facade panels, face fixed with screws | 32 – 33 |
| 15) ATK 103 + ATK 100 “Minor“ | Large and small format facade panels, with concealed fixings | 34 – 36 |
| 16) ATK 103 + ATK 100 ZeLa | Large and small format facade panels, with concealed fixings | 37 – 39 |
| 17) ATK 103 + ATK 100 Thermokonsole | Large and small format facade panels, with concealed fixings | 40 – 42 |
| 18) ATK 103 + ATK 101 | Large and small format facade panels, with concealed fixings | 43 – 45 |
| 19) ATK 103 + ATK 601 G | Large and small format facade panels, with concealed fixings | 46 – 48 |
| 20) ATK 104 + ATK 100 “Minor“ | Small-format panels visibly fixed with hooks from stainless steel | 49 – 51 |
| 21) ATK 104 + ATK 100 ZeLa | Small-format panels visibly fixed with hooks from stainless steel | 52 – 54 |
| 22) ATK 104 + ATK 100 Thermokonsole | Small-format panels visibly fixed with hooks from stainless steel | 55 – 56 |
| 23) ATK 104 + ATK 101 | Small-format panels visibly fixed with hooks from stainless steel | 57 – 59 |
| 24) ATK 104 + ATK 601 G | Small-format panels visibly fixed with hooks from stainless steel | 60 – 62 |

| Contents | Usability of the sub-structure | Page |
| --- | --- | --- |
| 25) ATK 110 + ATK 100 “Minor“ | Large-format facade panels fitted as weather boarding, visibly fixed | 63 – 65 |
| 26) ATK 110 + ATK 100 ZeLa | Large-format facade panels fitted as weather boarding, visibly fixed | 66 – 68 |
| 27) ATK 110 + ATK 100 Thermokonsole | Large-format facade panels fitted as weather boarding, visibly fixed | 69 – 70 |
| 28) ATK 110 + ATK 101 | Large-format facade panels fitted as weather boarding, visibly fixed | 71 – 73 |
| 29) ATK 110 + ATK 601 G | Large-format facade panels fitted as weather boarding, visibly fixed | 74 – 75 |
| 30) ATK 111 + ATK 100 “Minor“ | Large-format Trespa facade panels with concealed fixings | 76 – 78 |
| 31) ATK 111 + ATK 100 ZeLa | Large-format Trespa facade panels with concealed fixings | 79 – 81 |
| 32) ATK 111 + ATK 100 Thermokonsole | Large-format Trespa facade panels with concealed fixings | 82 – 84 |
| 33) ATK 111 + ATK 101 | Large-format Trespa facade panels with concealed fixings | 85 – 87 |
| 34) ATK 111 + ATK 601 G | Large-format Trespa facade panels with concealed fixings | 88 – 90 |
| 29) BWM-Fire inhibitors |  | 91 |

### A ) General Preliminary Remarks

The invitation to tender relates to the work for the supply and installation of a ventilated rainscreen facade.

The building has  ______ full storeys and a total height of ________ m.

The BWM sub-structure system is to be installed on walls made of e.g. concrete, brickwork etc.

_________________________________________________________________________________

Exact description of the anchoring substrate (if relevant, with an indication of any intermediate layers such as plaster, split tiles etc.)

Manufacturer of the sub-structures:

BWM

Dübel + Montagetechnik GmbH

P.O. Box 10 01 17

70745 Leinfelden-Echterdingen

Germany

Telephone:+49 (0)711/90 313-0

Fax:            +49 (0)711/90 313-20

Internet: www.bwm.de

The following building data are to be taken into account in order to determine

the wind loads according to DIN EN 1991-1-4 and DIN EN 1991-1-4/NA

| Wind zone: 1 / 2 / 3 or 4 |  |
| --- | --- |
| Category of the terrain: I , II, III or IV or mixed combination of coastal and inland terrain |  |
| Height above sea level: (only necessary if > 800 m above sea level) | ______ m |
| Main dimensions of building : W x H Building ground plan (see attachment) | ______ m x ______m |
| Building height above surface of ground | _______ m |
| Exposed position according to the standard? Yes / No. If Yes, exact description |  |
| Is building susceptible to vibration according to the Standard? Yes / No. If Yes, exact description |  |

On the basis of the above data, the wind loads are as follows:

On the side of the building ________At a height of           ______________

Wind pressure               __________ kN/m² acting on ……….% of total surface area

Wind suction in area A  __________ kN/m² acting on ……….% of total surface area

Wind suction in area B  __________ kN/m² acting on ……….% of total surface area

Wind suction in area C  __________ kN/m² acting on ……….% of total surface area

On the side of the building ________At a height of           ______________

Wind pressure               __________ kN/m² acting on ……….% of total surface area

Wind suction in area A  __________ kN/m² acting on ……….% of total surface area

Wind suction in area B  __________ kN/m² acting on ……….% of total surface area

Wind suction in area C  __________ kN/m² acting on ……….% of total surface area

All facades and surfaces of outer walls must be fitted with a ______  mm layer of thermal insulation as well as ventilated rainscreen facade cladding consisting of __________________________________ installed on an aluminium sub-structure.

Special care is to be taken with all the joints, panel connecting points and edges as well as the corners of the building.

The prices in the tender must include complete mounting and installation, including the necessary materials such as cladding panels, aluminium sections, anchoring/connecting/fixing components, sealing strips, accessory sections and other small parts, as well as wastage of off-cuts.

The sequence in which surfaces are to be covered as well as the sequence of mounting procedure is to be agreed with the construction supervisor.

The bidder undertakes to plan the dates and details with the construction supervisor in advance.

### B ) Standards and Guidelines to be observed

1)  DIN 18516 – External Wall Cladding, Ventilated, Part 1: Requirements, Test Principles

2)  VOB C ATV DIN 18299: General Regulations for Construction Works of All Types

3)  VOB C ATV DIN 18351: Suspended Ventilated Facades

### C) Quality Assurance during Construction

### Surcharge for quality assurance and control (BQA) during construction work in

### accordance with FVFH/ GTÜ industry standards and in accordance with the currently

### applicable table of fees.

### Lump Sum

| Sub-Structure system: | ATK 100 "Minor" |
| --- | --- |
| Uses: | - Vertical sub-structure for visible or bonded fixing of large-format facade panels - As a base sub-structure for horizontal support systems (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 100 “Minor“ made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of L-Brackets and supporting sections (material EN-AW 6063 T 66).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

fixed-point wall bracket per profile section in order to support the inherent weight of

the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The wall brackets are fitted with BWM stainless-steel retaining springs to facilitate

installation.

The supporting sections are connected to the wall brackets by means of BWM-

Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the wall brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 100 "Minor" |
| --- | --- |
| Uses: | - Vertical sub-structure for visibly (‘face’) fixed or bonded large- format facade panels - As a base sub-structure for horizontal support systems (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

L-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. __________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. __________m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 100 ZeLa |
| --- | --- |
| Uses: | - Vertical sub-structure for visibly (‘face’) fixed or bonded large- format facade panels - As a base sub-structure for Horizontal support systems (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 100 ZeLa made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of ZeLa facade brackets (material EN-AW 5754) and supporting sections

(material EN-AW 6063 T66).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Standard distances between wall and front surface of the sub-structure = 102 – 292

mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one ZeLa

fixed-point bracket (max. distance from the fixed point to the furthest sliding point =

2,50 m) per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by ZeLa sliding-point brackets

which enable an unforced change in length of the supporting sections due to

temperature changes.

The ZeLa facade brackets are fitted with BWM stainless-steel retaining springs to

facilitate mounting.

The supporting sections are connected to the ZeLa facade brackets by means of

BWM-Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Only approved anchoring elements are to be used for anchoring.
                             The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the ZeLa consoles and the anchoring substrate is to

be protected if required in accordance with DIN EN 1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 100 ZeLa |
| --- | --- |
| Uses: | - Vertical sub-structure for visibly (‘face’) fixed or bonded large- format facade panels - As a sub-structure for horizontal support systems (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. ________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

ZeLa facade brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Vertical sub-structure for visibly (‘face’) fixed or bonded large- format facade panels - As a sub-structure for horizontal support systems (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 100 Thermokonsole made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of the wall brackets Thermokonsole (material Ultramid A3WG10) and

aluminium supporting sections (material EN-AW 6063 T66).

The sub-structure is to be aligned in such a way that is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

Thermokonsole fixed-point bracket for each profile section to support the inherent

weight of the facade.

Wind pressure and suction forces are absorbed by Thermokonsole sliding-point

brackets which enable an unforced change in length of the supporting sections due

to temperature changes.

The Thermokonsole facade brackets are fitted with BWM stainless-steel retaining

springs to facilitate installation.

The supporting sections are connected to the Thermokonsole facade brackets by

means of BWM-Special rivets SNA 5x12K14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The requirements of the “General Technical Approval” or if the case arises of any

determinations issued for individual case approval relating to the applications of the

BWM Thermokonsole must be observed in particular with regard to any fire

protection requirements (permissible types of insulation, fire barriers, etc.).

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Vertical sub-structure for visibly (‘face’) fixed or bonded large- format facade panels - As a sub-structure for horizontal support systems (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 100 KL and KL-L |
| --- | --- |
| Uses: | - Vertical sub-structure for ceramic and fine stoneware panels with clamp fixings and 8mm joint |

TS item: _____  Adjustable aluminium sub-structure

System ATK 100 KL and KL-L made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of L-Brackets and supporting sections (material EN-AW 6063 T 66).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

fixed-point wall bracket per profile section in order to support the inherent weight of

the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The wall brackets are fitted with BWM stainless-steel retaining springs to facilitate

installation.

The supporting sections are connected to the wall brackets by means of BWM-

Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open, the width of the joints is 8 mm. The

unit prices must include stainless steel (A4) clamps, fasteners as well as techniques

to avoid clattering and migration of the facade panels.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the wall brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 100 KL and KL-L |
| --- | --- |
| Uses: | - Vertical sub-structure for ceramic and fine stoneware panels with clamp fixings and 8mm joint |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

L-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 101 |
| --- | --- |
| Uses: | - Vertical sub-structure for visibly (‘face’) fixed or bonded large- format facade panels - As a sub-structure for horizontal support systems (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 101 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of U-Brackets and supporting sections (material EN-AW 6063 T66).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The sub-structure sections are placed in the U-Brackets in a manner that they have

horizontal movement.

The supporting sections are to be installed vertically usually with one fixed-point wall

bracket per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The supporting sections are connected to the U-Brackets by means of BWM-Special

rivets SNA 5 x 12 K 14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open, the joint has an 8mm width. Stainless

steel clasps (A4) must be used.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 101 |
| --- | --- |
| Uses: | - Vertical sub-structure for visibly (‘face’) fixed or bonded large- format facade panels - As a sub-structure for horizontal support systems (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx.  _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 102 "Minor" |
| --- | --- |
| Uses: | - Vertical sub-structure for variable clamp fixing of facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 102 “Minor” made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of L-Brackets and supporting sections (material EN-AW 6063 T 66).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

fixed-point wall bracket per profile section in order to support the inherent weight of

the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The wall brackets are fitted with BWM stainless-steel retaining springs to facilitate

installation.

The supporting sections are connected to the wall brackets by means of BWM-

Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open, the width of the joints is variable.

Stainless steel clamps (A4) and spacers (A4) in addition to fixing elements and

EPDM profiles are to be included in the unit price.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 102 "Minor" |
| --- | --- |
| Uses: | - Vertical sub-structure for variable clamp fixing of facade panels |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

L-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 102 |
| --- | --- |
| Uses: | - Vertical sub-structure for variable clamp fixing of facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 102 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of U-Brackets and supporting sections (material EN-AW 6063 T66).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The sub-structure sections are placed in the U-Brackets in a manner that they have

horizontal movement.

The supporting sections are to be installed vertically usually with one fixed-point

wall bracket per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The supporting sections are connected to the U-Brackets by means of BWM-Special

rivets SNA 5 x 12 K 14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open, the width of the joints is variable.

Stainless steel clamps (A4) and spacers (A4) in addition to fixing elements and

EPDM profiles are to be included in the unit price.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 102 |
| --- | --- |
| Uses: | - Vertical sub-structure for variable clamp fixing of facade panels |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 102-GH |
| --- | --- |
| Uses: | - Vertical sub-structure for variable clamp fixing of toughened safety glass and photovoltaic glass elements |

TS item: _____  Adjustable aluminium sub-structure

System ATK 102-GH made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of U-Brackets and supporting sections (material EN-AW 6063 T66).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The sub-structure sections are placed in the U-Brackets in a manner that they have

horizontal movement.

The supporting sections are to be installed vertically usually with one fixed-point

wall bracket per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The supporting sections are connected to the U-Brackets by means of BWM-Special

rivets SNA 5 x 12 K 14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open.

Aluminium glass holder, clamps, glass-bearing brackets (EN-AW 6063 T66) in

addition to fixing elements and EPDM profiles are to be included in the unit price.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 102-GH |
| --- | --- |
| Uses: | - Vertical sub-structure for variable clamp fixing of toughened safety glass and photovoltaic glass elements |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 106 SZ 20 |
| --- | --- |
| Uses: | - Aluminium coffers with concealed fixings (‘secret fix’) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 106 SZ 20 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 106 SZ 20 made of aluminium

U-Brackets (material EN-AW 5754) and supporting sections

(material EN-AW 6063 T66)

or

vertical base support structure ATK 100 "Minor" made of aluminium

L-Brackets and supporting sections (material EN-AW 6063 T66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections ATK 106 SZ 20 or ATK 100 "Minor" are to be

installed vertically with one fixed-point wall bracket per profile section to support the

inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets

which enable an unforced change in length of the supporting sections due to

temperature changes.

The wall brackets are fitted with BWM stainless-steel retaining springs to facilitate

installation.

The supporting sections are connected to the wall brackets by means of BWM-

Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the wall brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 106 SZ 20 |
| --- | --- |
| Uses: | - Aluminium coffers with concealed fixings (‘secret fix’) |

B)    Horizontal support structure ATK 106 SZ 20 made of aluminium

supporting sections (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The joints of the supporting sections must correspond with the vertical joints of the

facade panels.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The facade panels are installed by means of the supporting sections fixed to the

reverse of the aluminium coffers and are mechanically secured against lateral

movement using SZ20 plastic clips in accordance with the manufacturer’s

recommendations.

When selecting the sub-structure the manufacturer’s recommendations of the

cladding panels are to be taken into consideration as well as the indications of

any Certificate or other Approval document.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

wall bracket referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

| Sub-Structure system: | ATK 106 SZ 20 |
| --- | --- |
| Uses: | - Aluminium coffers with concealed fixings (‘secret fix’) |

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 107 B |
| --- | --- |
| Uses: | - Vertical sub-structure for metal coffers with joints of width approx. ≤ 30 mm (inset bolt fixing) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 107 B made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of supporting sections and bolt sections (material EN-AW 6063 T66) as

well as U-Brackets type N-LW70 (material EN-AW 5754 H24/H34) and stainless-

steel bolts (A4).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The supporting sections are mounted in the U-Brackets type N-LW70.

The supporting sections are to be installed vertically usually with one fixed-point wall

bracket per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The supporting sections are connected to the U-Brackets by means of BWM-Special

rivets SNA 5 x 12 K 14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The bolts are installed in the required position using bolt sections, which are riveted

to the supporting sections.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 107 B |
| --- | --- |
| Uses: | - Vertical sub-structure for metal coffers with jointsof width approx. ≤ 30 mm (inset bolt fixing) |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 601 G |
| --- | --- |
| Uses: | - Vertical sub-structure for visible fixing of large-format facade panels - As base support structure for horizontal support structures (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 601 G made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of supporting sections and (material EN-AW 6063 T66) and fixing sets

consisting of M8 threaded bars, eye bolts, threaded sleeves, nuts and washers

made of stainless steel (A4).

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically with one fixed-point per

profile section to support the inherent weight of the facade.

These are installed with threaded bars and eye bolts according to the static

calculation.

Wind pressure and suction forces are absorbed by threaded bars, and the fixing

sets must be connected with the supporting sections in a stand-off installation.

According to the structural requirements additional bracings are mounted using

threaded bars and eye bolts.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed

points and sliding points, as well as all means of connecting and anchoring must be

in accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-Structure system: | ATK 601 G |
| --- | --- |
| Uses: | - Vertical sub-structure for visible fixing of large-format facade panels - As base support structure for horizontal support structures (ATK 103 / ATK 104 / ATK 110 / ATK 111) |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | Wood holder type H1 |
| --- | --- |
| Uses: | - Vertical wood sub-structures |

TS item: _____  Vertical adjustable aluminium / wood sub-structure

System type H1 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of U-Brackets (material EN-AW 5754 H24/H34) type H1.

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The wooden laths ____ x ____ mm in the joint area and ____ x ____ mm in surface

area of the cladding panels are mounted vertically using stainless steel screws, e.g.

(A4) - 5 x 40 according to DIN 571, in the pre-punched U-Brackets type H1

(4 per bracket).

Only approved anchoring elements are to be used for anchoring (one per bracket).

The distance between the wooden laths, U-Bracket spacings, dimensions of

U-Brackets, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the following

facade panels described below and the wind loads must be measured according to

DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required in accordance with DIN EN 1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

| Sub-structure system: | Wood holder type H1 |
| --- | --- |
| Uses: | - Vertical wood sub-structures |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction stress on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | Wood holders type T1,T2 |
| --- | --- |
| Uses: | - Vertical wood sub-structures |

TS item: _____  Vertical adjustable aluminium / wood sub-structure

System type T1,T2 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting L-Brackets (material EN-AW 6063 T66) or ZeLa facade brackets

(material EN-AW 5754) and T-shaped profiles (material EN-AW 6063 T66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The wooden laths ____ x ____ mm in the joint area and ____ x ____ mm in surface

area of the cladding panels are mounted vertically using stainless steel screws, e.g.

JT4-FR-2-4,9x35, in the pre-punched T-sections type T1, T2

(4 per bracket).

Only approved anchoring elements are to be used for anchoring.

The distance between the wooden laths, wall bracket spacings, dimensions of the

L-Brackets or ZeLa facade brackets, as well as all means of connecting and

anchoring must be in accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the following

facade panels described below and the wind loads must be measured according to

DIN.

The contact surface between the L-Brackets or ZeLa-consoles and the anchoring

substrate is to be protected if required in accordance with DIN EN 1991-1-1 and DIN

EN 1090-3.

Approx. _________ m2

| Sub-structure system: | Wooden holders type T1,T2 |
| --- | --- |
| Uses: | - Vertical wood sub-structures |

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

L-Brackets or ZeLa facade brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 103 + ATK 100 "Minor" |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 103 + ATK 100 Minor made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 100 Minor made of aluminium

L-Brackets and supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

fixed-point wall bracket per profile section in order to support the inherent weight of

the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The wall brackets are fitted with BWM stainless-steel retaining springs to facilitate

installation.

The supporting sections are connected to the wall brackets by means of BWM-

Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the wall brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 103 + ATK 100 "Minor" |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

B)    Horizontal support structure ATK 103 made of aluminium

supporting sections and clasps (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The joints of the supporting sections must correspond with the vertical joints of the

facade panels.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The facade panels are installed by means of the clasps fixed to the reverse surface

of the panels, adjusted by means of the set-screw contained in the clasp and

mechanically secured against lateral movement in accordance with the

manufacturer’s recommendations.

When selecting the sub-structure the manufacturer’s recommendations of the

cladding panels are to be taken into consideration as well as the indications of

any Certificate or other Approval document.

Approx. _________ m2

TS item: _____  As above, but the horizontal supporting sections are black anodized

(painting or powder coating the horizontal supporting sections is not recommended)

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

L-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. __________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. __________m

| Sub-structure system: | ATK 103 + ATK 100 "Minor" |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 103 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 103 + ATK 100 ZeLa made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 100 ZeLa made of aluminium

ZeLa facade brackets (material EN-AW 5754) and supporting sections

(material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Standard distances between wall and front surface of the sub-structure = 102 – 292

mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one ZeLa

fixed-point bracket (max. distance from the fixed point to the furthest sliding point =

2,50 m) per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by ZeLa sliding-point brackets

which enable an unforced change in length of the supporting sections due to

temperature changes.

The ZeLa facade brackets are fitted with BWM stainless-steel retaining springs to

facilitate mounting.

The supporting sections are connected to the ZeLa facade brackets by means of

BWM-Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Only approved anchoring elements are to be used for anchoring.
                             The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the ZeLa consoles and the anchoring substrate is to

be protected if required in accordance with DIN EN 1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 103 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

B)    Horizontal support structure ATK 103 made of aluminium

supporting sections and clasps (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The joints of the supporting sections must correspond with the vertical joints of the

facade panels.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The facade panels are installed by means of the clasps fixed to the reverse surface

of the panels, adjusted by means of the set-screw contained in the clasp and

mechanically secured against lateral movement in accordance with the

manufacturer’s recommendations.

When selecting the sub-structure the manufacturer’s recommendations of the

cladding panels are to be taken into consideration as well as the indications of

any Certificate or other Approval document.

Approx. _________ m2

TS item: _____  As above, but the horizontal supporting sections are black anodized

(painting or powder coating the horizontal supporting sections is not recommended)

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

ZeLa facade brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

| Sub-structure system: | ATK 103 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 103 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 103 + ATK 100 Thermokonsole made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 100 Thermokonsole

(material Ultramid A3WG10)

and aluminium supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

Thermokonsole fixed-point bracket for each profile section to support the inherent

weight of the facade.

Wind pressure and suction forces are absorbed by Thermokonsole sliding-point

brackets which enable an unforced change in length of the supporting sections due

to temperature changes.

The Thermokonsole facade brackets are fitted with BWM stainless-steel retaining

springs to facilitate installation.

The supporting sections are connected to the Thermokonsole facade brackets by

means of BWM-Special rivets SNA 5x12K14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The requirements of the “General Technical Approval” or if the case arises of any

determinations issued for individual case approval relating to the applications of the

BWM Thermokonsole must be observed in particular with regard to any fire

protection requirements (permissible types of insulation, fire barriers, etc.).

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 103 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

B)    Horizontal support structure ATK 103 made of aluminium

supporting sections and clasps (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The joints of the supporting sections must correspond with the vertical joints of the

facade panels.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The facade panels are installed by means of the clasps fixed to the reverse surface

of the panels, adjusted by means of the set-screw contained in the clasp and

mechanically secured against lateral movement in accordance with the

manufacturer’s recommendations.

When selecting the sub-structure the manufacturer’s recommendations of the

cladding panels are to be taken into consideration as well as the indications of

any Certificate or other Approval document.

Approx. _________ m2

TS item: _____  As above, but the horizontal supporting sections are black anodized

(painting or powder coating the horizontal supporting sections is not recommended)

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

| Sub-structure system: | ATK 103 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 103 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 103 + ATK 101 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 101 made of aluminium

U-Brackets and supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The sub-structure sections are placed in the U-Brackets in a manner that they have

horizontal movement.

The supporting sections are to be installed vertically usually with one fixed-point wall

bracket per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The supporting sections are connected to the U-Brackets by means of BWM-Special

rivets SNA 5 x 12 K 14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open, the joint has an 8mm width. Stainless

steel clasps (A4) must be used.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS Item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 103 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

B)    Horizontal support structure ATK 103 made of aluminium

supporting sections and clasps (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The joints of the supporting sections must correspond with the vertical joints of the

facade panels.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The facade panels are installed by means of the clasps fixed to the reverse surface

of the panels, adjusted by means of the set-screw contained in the clasp and

mechanically secured against lateral movement in accordance with the

manufacturer’s recommendations.

When selecting the sub-structure the manufacturer’s recommendations of the

cladding panels are to be taken into consideration as well as the indications of

any Certificate or other Approval document.

Approx. _________ m2

TS item: _____  As above, but the horizontal supporting sections are black anodized

(painting or powder coating the horizontal supporting sections is not recommended)

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

| Sub-structure system: | ATK 103 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 103 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 103 + ATK 601 G made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 601 G

aluminium supporting sections (material EN-AW 6063 T 66) and

fixing sets comprising M8 threaded bars, eye bolts, threaded sleeves,

nuts and washers made of stainless-steel (A4)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically with one fixed-point per

profile section to support the inherent weight of the facade.

These are installed with threaded bars and eye bolts according to the static

calculation.

Wind pressure and suction forces are absorbed by threaded bars, and the fixing

sets must be connected with the supporting sections in a stand-off installation.

According to the structural requirements additional bracings are mounted using

threaded bars and eye bolts.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed

points and sliding points, as well as all means of connecting and anchoring must be

in accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 103 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

B)    Horizontal support structure ATK 103 made of aluminium

supporting sections and clasps (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The joints of the supporting sections must correspond with the vertical joints of the

facade panels.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The facade panels are installed by means of the clasps fixed to the reverse surface

of the panels, adjusted by means of the set-screw contained in the clasp and

mechanically secured against lateral movement in accordance with the

manufacturer’s recommendations.

When selecting the sub-structure the manufacturer’s recommendations of the

cladding panels are to be taken into consideration as well as the indications of

any Certificate or other Approval document.

Approx. _________ m2

TS item: _____  As above, but the horizontal supporting sections are black anodized

(painting or powder coating the horizontal supporting sections is not recommended)

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

| Sub-structure system: | ATK 103 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of facade panels (‚secret fix‘) (Installation with clasps) |

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 104 + ATK 100 “Minor” |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 104 + ATK 100 “Minor” made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 100 Minor made of aluminium

L-Brackets and supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

fixed-point wall bracket per profile section in order to support the inherent weight of

the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The wall brackets are fitted with BWM stainless-steel retaining springs to facilitate

installation.

The supporting sections are connected to the wall brackets by means of BWM-

Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the wall brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 104 + ATK 100 “Minor” |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

B)    Horizontal support structure ATK 104 made of aluminium

supporting sections (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The unit prices must include stainless steel (A4) hooks and the fasteners.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

L-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. __________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. __________m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 104 + ATK 100 “Minor” |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-Structure system: | ATK 104 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 104 + ATK 100 ZeLa made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 100 ZeLa made of aluminium

ZeLa facade brackets (material EN-AW 5754) and supporting sections

(material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Standard distances between wall and front surface of the sub-structure = 102 – 292

mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one ZeLa

fixed-point bracket (max. distance from the fixed point to the furthest sliding point =

2,50 m) per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by ZeLa sliding-point brackets

which enable an unforced change in length of the supporting sections due to

temperature changes.

The ZeLa facade brackets are fitted with BWM stainless-steel retaining springs to

facilitate mounting.

The supporting sections are connected to the ZeLa facade brackets by means of

BWM-Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Only approved anchoring elements are to be used for anchoring.
                             The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the ZeLa consoles and the anchoring substrate is to

be protected if required in accordance with DIN EN 1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 104 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

B)    Horizontal support structure ATK 104 made of aluminium

supporting sections (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The unit prices must include stainless steel (A4) hooks and the fasteners.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

ZeLa facade brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 104 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 104 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Adjustable aluminium sub-structure system

ATK 104 + ATK 100 Thermokonsole made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 100 Thermokonsole

(material Ultramid A3WG10)

and aluminium supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

Thermokonsole fixed-point bracket for each profile section to support the inherent

weight of the facade.

Wind pressure and suction forces are absorbed by Thermokonsole sliding-point

brackets which enable an unforced change in length of the supporting sections due

to temperature changes.

The Thermokonsole facade brackets are fitted with BWM stainless-steel retaining

springs to facilitate installation.

The supporting sections are connected to the Thermokonsole facade brackets by

means of BWM-Special rivets SNA 5x12K14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The requirements of the “General Technical Approval” or if the case arises of any

determinations issued for individual case approval relating to the applications of the

BWM Thermokonsole must be observed in particular with regard to any fire

protection requirements (permissible types of insulation, fire barriers, etc.).

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 104 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

B)    Horizontal support structure ATK 104 made of aluminium

supporting sections (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The unit prices must include stainless steel (A4) hooks and the fasteners.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 104 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 104 + ATK 101 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 101 made of aluminium

U-Brackets and supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The sub-structure sections are placed in the U-Brackets in a manner that they have

horizontal movement.

The supporting sections are to be installed vertically usually with one fixed-point wall

bracket per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The supporting sections are connected to the U-Brackets by means of BWM-Special

rivets SNA 5 x 12 K 14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open, the joint has an 8mm width. Stainless

steel clasps (A4) must be used.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 104 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

B)    Horizontal support structure ATK 104 made of aluminium

supporting sections (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The unit prices must include stainless steel (A4) hooks and the fasteners.

The average distance between the wall and the front surface of the sub-structure is

______mm.

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 104 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 104 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 104 + ATK 601 G made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 601 G

aluminium supporting sections (material EN-AW 6063 T 66) and

fixing sets comprising M8 threaded bars, eye bolts, threaded sleeves, nuts and washers made of stainless-steel (A4)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically with one fixed-point per

profile section to support the inherent weight of the facade.

These are installed with threaded bars and eye bolts according to the static

calculation.

Wind pressure and suction forces are absorbed by threaded bars, and the fixing

sets must be connected with the supporting sections in a stand-off installation.

According to the structural requirements additional bracings are mounted using

threaded bars and eye bolts.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed

points and sliding points, as well as all means of connecting and anchoring must be

in accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 104 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

B)    Horizontal support structure ATK 104 made of aluminium

supporting sections (material EN-AW 6063 T66)

The horizontal supporting sections are installed on the vertical base support

structure at the required fixing intervals according to the static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The unit prices must include stainless steel (A4) hooks and the fasteners.

The average distance between the wall and the front surface of the sub-structure is

______mm.

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 104 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for hook fixing of small-format facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 110 + ATK 100 “Minor“ |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

TS Item: _____  Adjustable aluminium sub-structure

System ATK 110 + ATK 100 “Minor“ made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 100 Minor made of aluminium

L-Brackets and supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

fixed-point wall bracket per profile section in order to support the inherent weight of

the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The wall brackets are fitted with BWM stainless-steel retaining springs to facilitate

installation.

The supporting sections are connected to the wall brackets by means of BWM-

Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the wall brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 110 + ATK 100 “Minor“ |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

B)    Horizontal support structure ATK 110 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections for 8 mm panels are installed on the

vertical base support structure at intervals of _____mm.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

L-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. __________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. __________m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 110 + ATK 100 “Minor“ |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 110 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 110 + ATK 100 ZeLa

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 100 ZeLa made of aluminium

ZeLa facade brackets (material EN-AW 5754) and supporting sections

(material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Standard distances between wall and front surface of the sub-structure = 102 – 292

mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one ZeLa

fixed-point bracket (max. distance from the fixed point to the furthest sliding point =

2,50 m) per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by ZeLa sliding-point brackets

which enable an unforced change in length of the supporting sections due to

temperature changes.

The ZeLa facade brackets are fitted with BWM stainless-steel retaining springs to

facilitate mounting.

The supporting sections are connected to the ZeLa facade brackets by means of

BWM-Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Only approved anchoring elements are to be used for anchoring.
                             The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the ZeLa consoles and the anchoring substrate is to

be protected if required in accordance with DIN EN 1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 110 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

B)    Horizontal support structure ATK 110 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections for 8 mm panels are installed on the

vertical base support structure at intervals of _____mm.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

ZeLa facade brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 110 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 110 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 110 + ATK 100 Thermokonsole made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 100 Thermokonsole

(material Ultramid A3WG10)

and aluminium supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

Thermokonsole fixed-point bracket for each profile section to support the inherent

weight of the facade.

Wind pressure and suction forces are absorbed by Thermokonsole sliding-point

brackets which enable an unforced change in length of the supporting sections due

to temperature changes.

The Thermokonsole facade brackets are fitted with BWM stainless-steel retaining

springs to facilitate installation.

The supporting sections are connected to the Thermokonsole facade brackets by

means of BWM-Special rivets SNA 5x12K14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The requirements of the “General Technical Approval” or if the case arises of any

determinations issued for individual case approval relating to the applications of the

BWM Thermokonsole must be observed in particular with regard to any fire

protection requirements (permissible types of insulation, fire barriers, etc.).

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 110 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

B)    Horizontal support structure ATK 110 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections for 8 mm panels are installed on the

vertical base support structure at intervals of _____mm.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 110 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

TS item: _____  Adjustable aluminium-sub-structure system

System ATK 110 + ATK 101 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 101 made of aluminium

U-Brackets and supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The sub-structure sections are placed in the U-Brackets in a manner that they have

horizontal movement.

The supporting sections are to be installed vertically usually with one fixed-point wall

bracket per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The supporting sections are connected to the U-Brackets by means of BWM-Special

rivets SNA 5 x 12 K 14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open, the joint has an 8mm width. Stainless

steel clasps (A4) must be used.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 110 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

B)    Horizontal support structure ATK 110 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections for 8 mm panels are installed on the

vertical base support structure at intervals of _____mm.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 110 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 110 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

TS Item: _____  Adjustable aluminium sub-structure

System ATK 110 + ATK 601 G made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 601 G

aluminium supporting sections (material EN-AW 6063 T 66) and

fixing sets comprising M8 threaded bars, eye bolts, threaded sleeves, nuts and washers made of stainless-steel (A4)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically with one fixed-point per

profile section to support the inherent weight of the facade.

These are installed with threaded bars and eye bolts according to the static

calculation.

Wind pressure and suction forces are absorbed by threaded bars, and the fixing

sets must be connected with the supporting sections in a stand-off installation.

According to the structural requirements additional bracings are mounted using

threaded bars and eye bolts.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed

points and sliding points, as well as all means of connecting and anchoring must be

in accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 110 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure with weather boarding for visible fixing of 8mm facade panels |

B)    Horizontal support structure ATK 110 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections for 8 mm panels are installed on the

vertical base support structure at intervals of _____mm.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 111 + ATK 100 “Minor“ |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 111 + ATK 100 “Minor“ made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 100 Minor made of aluminium

L-Brackets and supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

fixed-point wall bracket per profile section in order to support the inherent weight of

the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The wall brackets are fitted with BWM stainless-steel retaining springs to facilitate

installation.

The supporting sections are connected to the wall brackets by means of BWM-

Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the wall brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 111 + ATK 100 “Minor“ |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

B)    Horizontal support structure ATK 111 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections are installed on the vertical base

support structure at the required intervals according to a static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

A backing strip is glued onto the horizontal sections according to the facade panel

manufacturer’s recommendations.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

L-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. __________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. __________m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 111 + ATK 100 “Minor“ |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 111 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 111 + ATK 100 ZeLa made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

A)    Vertical base support structure ATK 100 ZeLa made of aluminium

ZeLa facade brackets (material EN-AW 5754) and supporting sections

(material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Standard distances between wall and front surface of the sub-structure = 102 – 292

mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one ZeLa

fixed-point bracket (max. distance from the fixed point to the furthest sliding point =

2,50 m) per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by ZeLa sliding-point brackets

which enable an unforced change in length of the supporting sections due to

temperature changes.

The ZeLa facade brackets are fitted with BWM stainless-steel retaining springs to

facilitate mounting.

The supporting sections are connected to the ZeLa facade brackets by means of

BWM-Special rivets SNA 5 x 12 K 14 A/N or self-drilling screws JT4-3H/5-5,5x19.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet or screw fixing in accordance with the Building

Regulation List A Part 2, Point 2.17.

Only approved anchoring elements are to be used for anchoring.
                             The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the ZeLa consoles and the anchoring substrate is to

be protected if required in accordance with DIN EN 1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 111 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

B)    Horizontal support structure ATK 111 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections are installed on the vertical base

support structure at the required intervals according to a static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

A backing strip is glued onto the horizontal sections according to the facade panel

manufacturer’s recommendations.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

ZeLa facade brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 111 + ATK 100 ZeLa |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 111 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

TS item: _____  Adjustable aluminium sub-structure

System ATK 111 + ATK 100 Thermokonsole made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 100 Thermokonsole

(material Ultramid A3WG10)

and aluminium supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically usually with one

Thermokonsole fixed-point bracket for each profile section to support the inherent

weight of the facade.

Wind pressure and suction forces are absorbed by Thermokonsole sliding-point

brackets which enable an unforced change in length of the supporting sections due

to temperature changes.

The Thermokonsole facade brackets are fitted with BWM stainless-steel retaining

springs to facilitate installation.

The supporting sections are connected to the Thermokonsole facade brackets by

means of BWM-Special rivets SNA 5x12K14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The requirements of the “General Technical Approval” or if the case arises of any

determinations issued for individual case approval relating to the applications of the

BWM Thermokonsole must be observed in particular with regard to any fire

protection requirements (permissible types of insulation, fire barriers, etc.).

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 111 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

B)    Horizontal support structure ATK 111 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections are installed on the vertical base

support structure at the required intervals according to a static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

A backing strip is glued onto the horizontal sections according to the facade panel

manufacturer’s recommendations.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 111 + ATK 100 Thermokonsole |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 111 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

TS item: _____  Adjustable aluminium sub structure

System ATK 111 + ATK 101 made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 101 made of aluminium

U-Brackets and supporting sections (material EN-AW 6063 T 66)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of:

__________________________________________________________________

Please give an exact description

The sub-structure sections are placed in the U-Brackets in a manner that they have

horizontal movement.

The supporting sections are to be installed vertically usually with one fixed-point wall

bracket per profile section in order to support the inherent weight of the facade.

Wind pressure and suction forces are absorbed by sliding-point wall brackets which

enable an unforced change in length of the supporting sections due to temperature

changes.

The supporting sections are connected to the U-Brackets by means of BWM-Special

rivets SNA 5 x 12 K 14 A/N.

An approved “General Building Authority Test Certificate” according to DIN is to be

submitted for this type of rivet fixing in accordance with the Building Regulation

List A Part 2, Point 2.17.

Suitable rivet-setting gauge attachments are to be used when riveting the sliding

points in accordance with the manufacturer's instructions.

The vertical and horizontal joints remain open, the joint has an 8mm width. Stainless

steel clasps (A4) must be used.

Only approved anchoring elements are to be used for anchoring.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed points

and sliding points, as well as all means of connecting and anchoring must be in

accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

The contact surface between the U-Brackets and the anchoring substrate is to be

protected if required according to DIN EN-1991-1-1 and DIN EN 1090-3.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 111 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

B)    Horizontal support structure ATK 111 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections are installed on the vertical base

support structure at the required intervals according to a static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

A backing strip is glued onto the horizontal sections according to the facade panel

manufacturer’s recommendations.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  Thermostop

Placing additional thermal separators of the type BWM Thermostop for the

U-Brackets referred to

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 111 + ATK 101 |
| --- | --- |
| Uses: | - Sub-structure for concealed fixing of large format Trespa (TS300) facade panels |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | ATK 111 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for the concealed fixing of large-format Trespa facade panels (TS300) |

TS item: _____  Adjustable aluminium sub-structure

System ATK 111 + ATK 601 G made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Vertical base support structure ATK 601 G

aluminium supporting sections (material EN-AW 6063 T 66) and

fixing sets comprising M8 threaded bars, eye bolts, threaded sleeves, nuts and washers made of stainless-steel (A4)

The sub-structure is to be aligned in such a way that it is in true alignment and

vertical.

The average distance between the wall and the front surface of the sub-structure is

______mm.

The anchoring substrate consists of

__________________________________________________________________

Please give an exact description

The BWM supporting sections are to be installed vertically with one fixed-point per

profile section to support the inherent weight of the facade.

These are installed with threaded bars and eye bolts according to the static

calculation.

Wind pressure and suction forces are absorbed by threaded bars, and the fixing

sets must be connected with the supporting sections in a stand-off installation.

According to the structural requirements additional bracings are mounted using

threaded bars and eye bolts.

The joints of the supporting sections must correspond with the horizontal joints of

the facade panels.

Types of supporting section and distances between them, dimensions of fixed

points and sliding points, as well as all means of connecting and anchoring must be

in accordance with a static calculation.

The sub-structure is to be designed for the inherent weight loads of the facade

panels described below, and the wind loads are to be measured according to DIN.

Approx. _________ m2

TS item: _____  As above, but the vertical supporting sections are black anodized

Approx. _________ m2

| Sub-structure system: | ATK 111 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for the concealed fixing of large-format Trespa façade panels (TS300) |

B)    Horizontal support structure ATK 111 made of aluminium

supporting sections (material EN-AW 6063 T66)

The ATK 110 horizontal supporting sections are installed on the vertical base

support structure at the required intervals according to a static calculation.

The horizontal supporting sections are fixed by using DIN approved BWM-Special

rivets SNA 5x12 K14 A/N. For each horizontal section a fixed-point rivet is to be set

in a round hole, all other rivets are to be made in the oblong holes using rivet-setting

gauge attachments.

A backing strip is glued onto the horizontal sections according to the facade panel

manufacturer’s recommendations.

The average distance between the wall and the front surface of the sub-structure is

______mm.

Approx. _________ m2

TS item: _____  Areas with increased wind loads

For the reinforcement of the sub-structure necessary due to increased wind

suction loads on buildings according to DIN

Approx. _________ m2

TS item: _____  External corners

Addition to the sub-structure for forming external corners

Approx. _________ m

TS item: _____  Internal corners

Addition to the sub-structure for forming internal corners

Approx. _________ m

TS item: _____  Embrasures and reveals

Addition to the sub-structure for forming the window embrasures and door reveals

with a width of _______ cm

Approx. _________ m

TS item: _____  Building expansion joints

Addition to the sub-structure construction for forming in the area of building

expansion joints

Approx. __________ m

| Sub-structure system: | ATK 111 + ATK 601 G |
| --- | --- |
| Uses: | - Sub-structure for the concealed fixing of large-format Trespa facade panels (TS300) |

TS item: _____  Submission of a competent building-specific static calculation

Lump Sum

Other items for the sub-structure may be necessary depending on the actual

features of the building and its situation.

| Sub-structure system: | BWM Fire Barriers |
| --- | --- |
| Uses: | - For increased requirements for fire protection of ventilated rain screen facades |

TS item: _____  Fire barriers made by

BWM

Dübel + Montagetechnik GmbH

P.O. Box 100 117

70745 Leinfelden-Echterdingen

Germany

Telephone: +49(0)711 – 90 313-0

Fax: +49(0)711 – 90 313-20

Supply and install in accordance with DIN 18516, using the original parts indicated,

consisting of

- Wall section 30 mm x 40….370 mm made of 1,0 mm galvanized iron

- Ventilation section made of 1,0 mm galvanized iron

- Fasteners for ventilation section made of galvanized iron

The fire barriers are installed in accordance with the respective Building Control

Authority / Regional Building Control.

The installation of the wall sections is undertaken using permissible approved

anchoring elements in pre-punched oblong holes into the anchoring substrate

made of _____________ .

The ventilation sections are fixed to the wall sections using rivets.

An additional fixing of the ventilation profiles is achieved through the use of

fasteners, which are connected sideways on the sections present on the building

using screws / rivets.

All fixing intervals and the installation lengths of the sections are according to

The manufacturer’s recommendations.

Approx. _________ m